## Slide 1: FAI/CIA Event Logger Project
New Technology Working Group – Lausanne, March 2009

## Slide 2: Why new GPS Loggers?
Most current loggers are in bad condition
Improve ballooning competitions
  Virtual marker drops
  Fly On tasks
Stop / reduce discussions about accuracy
  State of the art GPS technology (SiRF III)
  Pilot can view his logged position
  Logger interval 1sec
Simplify logger handling in scoring

## Slide 3: Key features
Display position, altitude, marker status
Keypad to enter Fly On goals or drop markers
USB-Port to use logger as navigation device for the pilot’s laptop
SD-Card to store the digitally signed track
Serial output for telemetry (live tracking/scoring)
SiRF III newest GPS technology available

## Slide 4: Collaboration with Flytec
In April 2008 we started a collaboration with Flytec
We can use their 6020 hardware and write our own custom software
  Hardware is already in use and stable
  The device has all necessary components
  Graphical display, custom keypad
  Low power (30h runtime)
  Very good barometric altitude
Documentation, calibration warranty and support from Flytec

## Slide 5: Logger Hardware
SD-Card slot
160x240 display
USB-connection
Custom keypad

## Slide 6: Custom Keypad
Fast marker drop
Simple navigation
Easy goal declaration

## Slide 7: Easy handling
Handling is very easy
The following actions are possible:
  Drop a marker (markers are numbered 1..9)
  Declare a goal (1..9)
  List dropped markers and declared goals
Barometric altitude
The idle screen shows all necessary information.
Coordinates can also be displayed in UTM and altitude in feet.

## Slide 8: Marker drop
1. Press „Drop Marker“
2. Select Marker number
The user gets a warning if he already dropped the same marker before.
3. Press ok to drop marker
You can wait here as long as you want until your are closest to the target
4. The idle screen shows the dropped markers

## Slide 9: Goal declaration
2. Enter goal coordinates.
The logger accepts either goal number or coordinates. Altitude is optional.
1. Select „Declare Goal“ and select the goal number
A list of goals (and markers) can be displayed
The declaration is stored together with a timestamp!

## Slide 10: Comparison
 | New FAI Event Logger | Other retail loggers
See the actual scored altitude | + | Requires laptop
Electronic mark | + | Very few yes, but can’t differentiate between marks or tasks
FON and PDG | + | -
Fraud protection | + | Very limited, not tamperproof
Accurate altitude measurement | + | A few yes, most no
Easy handling (preflight, during flight and at debriefing) | + | A few yes, depending on competition operation procedures
Instant feedback in case of logger problems | + | -
Rechargeable batteries | + | Huge waste, ecologically not reasonable
Quality of devices, life cycle | + | Some bad quality, max 4-5 years
Extensibility (add features) | + | -
control over software functionalities | + | -

## Slide 11: Cost & Financing
Cost per device: ±530€
Sponsor or financial partner to pay for devices
Rent to event organizers

## Slide 12: Timing
2009
Find a sponsor or financial partner
Build a first series of about 40 devices
Start renting model in some events
Build more devices to be used in continental or world championship
2010
Build more devices to complete set of 150